## Slide 1
Lecturer: Nana Liu
Summer 2020
Chapter 7:
Time-Varying Fields and
Maxwell’s Equations
Many slides courtesy of Sung-Liang Chen

## Slide 2
Everything you need to know
about time-varying fields
and Maxwell’s equations
in this course…

## Slide 3
Yay!!!
Finally the whole T-shirt!!!

## Slide 4
Main parts in time-varying fields:
(I) Modifying 2 Maxwell’s equations away from static case: moving currents and magnets
(II) Electromagnetic waves
(III) Electromagnetic boundary conditions
(IV) Solutions for wave equations

## Slide 5
Maxwell’s Equations

## Slide 6
Maxwell’s Equations

## Slide 7
Time-varying fields scenarios:
Static circuit in moving B field
Moving conductor in static B field
Circuit and B field both in motion

## Slide 8
Time-varying fields scenarios:
EMF

## Slide 9
Maxwell’s Equations

## Slide 10
Vector and scalar potentials

## Slide 11
Vector and scalar potentials
Poisson’s equations (static cases)
Wave equations (time-varying cases)

## Slide 12
Source-free wave solutions
Homogeneous vector wave equations

## Slide 13
Boundary conditions

## Slide 14: 7-1 Introduction
Electrostatics:
Magnetostatics:
For linear and isotropic media
For linear and isotropic media

## Slide 16: Static Case
(E and D) and (B and H) form separate and independent pairs.
Electromagnetostatic field: in a conducting medium, static E  static J  static B.
  Static electric and static magnetic fields both exist.
  B is a consequence, not affecting E

## Slide 17: Time-varying Case
(E and D) and (B and H) are related.
A changing magnetic field gives rise to an electric field, and vice versa.
Table 7-1 must be modified.

## Slide 18: 7-2 Faraday’s Law of Electromagnetic Induction
Faraday’s law: the quantitative relationship between the induced emf and the rate of change of flux linkage, based on experimental observation (emf = d/dt).
Fundamental postulate for electromagnetic induction:
  Applies whether it be in free space or in a material medium
  The electric field intensity in a region of time-varying magnetic flux density is therefore nonconservative and cannot be expressed as the gradient of a scalar potential

## Slide 19
Surface integral over an open surface
Stokes’ theorem
Integral form

## Slide 20: Several Cases
A stationary circuit in a time-varying magnetic field (transformer emf)
A moving conductor in a static magnetic field (motional emf)
A moving circuit in a time-varying magnetic field (combined)

## Slide 21: 7-2.1 A Stationary Circuit in a Time-Varying Magnetic Field
For a stationary circuit with a contour C and surface S
  Define
Stationary S (i.e., S not a function of time)
C may or may not be a physical circuit

## Slide 22
  Then,
Faraday’s law of electromagnetic induction: The emf induced in a stationary closed circuit is equal to the negative rate of increase of the magnetic flux linking the circuit. (Transformer emf)
The induced emf will cause a current to flow in the closed loop in such a direction as to oppose the change in the linking magnetic flux. (Lenz’s law)

## Slide 23: Example

## Slide 24: Example

## Slide 25: Example

## Slide 26: 7-2.2 Transformers
A transformer: two or more coils coupled magnetically through a common ferromagnetic core.

## Slide 27
KVL for magnetic circuit:
By Lenz’s law, the induced mmf, N2i2, opposes flux  created by the mmf in the primary circuit, N1i1.
Primary circuit
Secondary circuit

## Slide 28: Ideal transformer
Assume   ,
The ratio of the currents in the primary and secondary windings of an ideal transformer is equal to the inverse ratio of the numbers of turns.

## Slide 29
The ratio of the voltages across the primary and secondary windings of an ideal transformer is equal to the turns ratio.
From Faraday’s law:

## Slide 30: 7-2.3 A Moving Conductor in a Static Magnetic Field
A magnetic force
Moving velocity of a conductor
Static magnetic field

Fm=qEm
+
Fm (magnetic force)  charge separation  Einduced Fe (electric force)
At equilibrium, the net force (Fm+Fe) on the free charges in the moving conductor is zero.
Fe=qEinduced

## Slide 31

Fm=qEm
+
Fe=qEinduced
Called flux cutting emf or motional emf
For u//B (no flux is cut), emf V’=0
If the moving conductor is a part of a closed circuit C, the emf
An induced electric field acting along the conductor and producing a voltage
Einduced=Em=uB

## Slide 32: 7-2.4 A Moving Circuit in a Time-Varying Magnetic Field
Transformer emf + motional emf
Lorentz’s force equation:
The effective electric field E’ on q:
Due to time-varying magnetic field (transformer emf)
Due to a moving circuit (motional emf)

## Slide 33
Considering a conducting circuit with contour C and surface S moves with a velocity u in a field (E,B):
General form of Faraday’s law for a moving circuit in a time-varying magnetic field.
Integral along C
and use
Transformer emf
Motional emf
(34)

## Slide 34: A Moving Circuit
The contour C moves from C1 at time t to C2 at time t+t
The motion can be translation, rotation, and distortion in an arbitrary manner.
Moving velocity: u

## Slide 35
Expand this term B(t+t) as a Taylor’s series
(2)
(1)
(1)
(2)
(3)
(3)
(4)
(4)
(37)

## Slide 36
In going from C1 to C2, the circuit covers a region bound by S1, S2, and S3.
S3: side surface, the area swept out by the contour in time t. An element of S3
Apply the divergence theorem for B at time t
ds1
ds2
Because outward normal must be used

## Slide 37
0
(40)
A(BC) = B(CA)

## Slide 38
(37)
(40)
Combine Eqs. (37) and (40)
H.O.T is neglected as t0
Compared with (34)


## Slide 39

By designating
(43)

## Slide 40: Comparison of Eqs. (43) and (6)
(43)
(6)
They are exactly the same.
V’ is for circuits in motion; V is for circuits not in motion
Faraday’s law that the emf induced in a closed circuit equals the negative time-rate of increase of the magnetic flux linking a circuit applies to a stationary circuit as well as a moving one.

## Slide 41: Example

## Slide 42: Example

## Slide 43: Example

## Slide 44: Example

## Slide 45: Example

## Slide 46: Example

## Slide 47: 7-3 Maxwell’s Equations
Electromagnetic induction: a time-varying magnetic field gives rise to an electric field.
Static case
Time-varying case

## Slide 48: Modification of H=J in a Time-varying Case
Charge conservation (or the equation of continuity) must be satisfied at all times
Check if H=J is consistent with the requirement of charge conservation in a time-varying situation
By null identity

## Slide 49
Since J=0 does not vanish in a time-varying situation (or  is changing in a time-varying situation), J=0 is in general not true.
 H=J should be modified in a time-varying situation

In order to satisfy
Not consistent!

## Slide 50
Thus, a time-varying electric field will give rise to a magnetic field, even in the absence of a current flow.
A short summary:
To satisfy charge conservation
Displacement current density
(Introduced by James Clerk Maxwell)

## Slide 51: Maxwell’s Equation
: free charge
J: free currents (including convection current (u) and conduction current (E))
The above 6 equations form the foundation of electromagnetic theory!

## Slide 52: Electromagnetic Problem
4 unknowns: E, D, B, H
4 independent equations
(1) and
(2)
(3)
(4)

## Slide 53: 7-3.1 Integral Form of Maxwell’s Equations
Surface integral
Stokes’ theorem
Volume integral
Divergence theorem

## Slide 55: 7-4 Potential Functions
or
divergenceless

## Slide 56
curl free
Due to charge distribution   V
Due to time-varying current J  A
V and A here are solutions of Poisson’s equations

## Slide 57: Quasi-static Fields
The two equations were obtained under static conditions
They can be time dependent: (t), J(t)  V(t), A(t)
If  and J vary slowly with time and the range of interest R is small in comparison with the wavelength (low frequency, long wavelength), it is allowable to use the 2 equations to find quasi-static fields.

## Slide 58: Time-retardation Effects
Quasi-static fields are approximations.
When the source frequency is high, quasi-static solutions will not suffice. Time-retardation effects must be included. (Discussed in 7-6)

## Slide 59
0
=0sin(t)
V(a)
a
t
a
V(a)
t


Time-retardation effects for high-frequency sources
As the source changes in time, it takes time to change the potential at a certain distance from the source!

## Slide 60
Assume a homogeneous medium
Vector identity
or
B=

## Slide 61
A vector requires the specification of both its curl and its divergence.
  Curl has been specified
  How to choose divergence!?
We let
Nonhomogeneous wave equation for vector potential A
Reduced to Poisson’s equation for static cases
Its solutions represent waves traveling with a velocity (Discussed more in 7-6)
Lorentz condition (or Lorentz gauge) for potentials
Also, the condition is consistent with equation of continuity (P7-12)

## Slide 62
Nonhomogeneous wave equation for scalar potential V
Assume a constant 
Reduced to Poisson’s equation in static cases
Its solutions represent waves traveling with a velocity
Lorentz condition uncouples the wave equations for A and V

## Slide 63: Solution of Wave Equations for A and V
Poisson’s equations (static cases)
Wave equations (time-varying cases)
Solutions
Solutions ?
Different equations  solutions must be modified! (Discussed more in 7-6)

## Slide 64: 7-5 Electromagnetic Boundary Conditions
In general, the application of the integral form of a curl equation to a flat closed path at a boundary with top and bottom sides in the two touching media yields the boundary condition for the tangential components
The application of the integral form of a divergence equation to a shallow pillbox at an interface with top and bottom faces in the two contiguous media gives the boundary condition for the normal components

## Slide 65
For curl equations:
Let the height of the flat closed path approach zero (area  0)
 The surface integral of B/t and D/t vanishes
 Same as equations for static electric and static magnetic fields
h

## Slide 66
The tangential component of an E field is continuous across an interface
The tangential component of an H field is discontinuous across an interface where a surface current exists, the amount of discontinuity being determined by Eq. (2)
The normal component of a D field is discontinuous across an interface where a surface charge exists, the amount of discontinuity being determined by Eq. (3)
The normal component of a B field is continuous across an interface
(2)
(3)

## Slide 67
Equivalent BC
Equivalent BC
Due to the dependence of Maxwell’s equations, divergence equations can be derived from curl equations and equation of continuity.

## Slide 68: 7-5.1 Interface between Two Lossless Linear Media
A lossless linear media: , , =0
  J=0  power dissipation = 0  lossless
Usually no free charges and no surface currents at the interface of two lossless media. (s=0, Js=0)

## Slide 69: 7-5.2 Interface between a Dielectric and a Perfect Conductor
Conductors
  Good conductors:  ~ 107 (S/m)
  Superconductors:  ~ 1020 (S/m)
In order to simplify the analytical solution of field problems, good conductors are often considered perfect conductors in regard to boundary conditions.

## Slide 70: Perfect Conductors
  
Einside = 0 (otherwise, infinite J inside)
Charges only reside on the surface
In a time-varying situation, (E, D) and (B, H) in the interior of a conductor are zero.
  E=0  D=0
  E=0  B(t)=0 B=0  H=0
in the static case, B and H may not be zero!
In a time-varying situation, B should be time varying (i.e., cannot be a nonzero constant)!

## Slide 71
In medium 2 (a perfect conductor), E2=0, H2=0, D2=0, B2=0
Q: How about if medium 2 is a conductor with finite conductivity?
A: As mentioned in Section 6-10, currents in media with finite conductivities are expressed in terms of volume current densities J, and surface current densities JS for currents flowing through an infinitesimal thickness (t) is zero.
Js=J*t=0 as t0 (t: thickness)
Ht continuous

## Slide 72
E1t=0  E is normal to the points away from (into) the conductor surface when the surface charges are positive (negative)

## Slide 73: Importance of Boundary Conditions
Maxwell’s equations are partial differential equations. Their solutions will contain integration constants that are determined from the additional information supplied by boundary conditions so that each solution will be unique for each given problem.

## Slide 74: 7-6 Wave Equations and Their Solutions
Importance of Maxwell’s equations
  Give a complete description of the relation between electromagnetic fields and charge and current distributions (sources).
  Their solutions provide the answers to all electromagnetic problems.
For given charge and current distributions

J
V
A
E, B

## Slide 75: 7-6.1 Solution of Wave Equations for Potentials
Nonhomogeneous wave equation
Finding V for an elemental point charge at time t located at the origin
  Spherical symmetry  V(R,t) is only function of R
  Except at origin, the wave equation

## Slide 76
Introduce a new variable U
A 1D homogeneous wave eq.
Solution, which can be verified by direct substitution
“” solution doesn’t satisfy causality and thus is neglected. (Discussed later.)
(7-71)
(7-74)

## Slide 77
Check the function U at R+R at a later time t+t
The function retains its form If
Thus, the function U(R,t) represents a wave traveling in the positive R direction with a velocity u = R/t =

## Slide 79
Next, to determine the specific function
A static point charge (t)v’ at origin
Comparison with
Potential due to a charge distribution
(integration)
Incorporate the retardation effect !
R

## Slide 80
The value of  at an earlier time (tR/u)
 V(R,t) at a distance R from the source at time t
It takes time R/u for the effect of  to be felt at distance R.
That is, there is time retardation (t  R/u) from  to V

V(R,t)
R=ut
Q: can you explain now why “+” cannot be a solution?
A: it would lead to the impossible situation that the effect of  would be felt at a distant point before it occurs at the source. (or “” solution doesn’t satisfy causality.)

## Slide 81
Following exactly the same way as that for V
Wave equation
Wave equation
Retarded V
Retarded A

## Slide 82
E or B obtained from V and A will also be functions of (tR/u) and therefore retarded in time.
It takes time for electromagnetic waves to travel and for the effects of time-varying charges and currents to be felt at distant points.
In the quasi-static approximation we ignore this time-retardation effect and assume instant response.

## Slide 83: 7-6.2 Source-Free Wave Equations
Source free: =0, J=0
Often interested not so much in how an electromagnetic wave is originated, but in how it propagates.
Assuming a simple nonconducting media characterized by  and  (=0),
D=E
B=H

## Slide 84
Curl on both sides
In an entirely similar way,
.
.
.
Homogeneous vector wave equations
substitute

## Slide 85
In Cartesian coordinates, the above equations can be decomposed into three 1D wave equations, just like the equation (7-73) solved before
Thus, each component of E and H also represents waves, just like U.
Homogeneous vector wave equations

## Slide 86: 7-7 Time-Harmonic Fields
Since Maxwell’s equations are linear differential equations, sinusoidal time variations of source functions of a given frequency will produce sinusoidal variations of E and H with the same frequency in the steady state.
For source functions with an arbitrary time dependence, electrodynamic fields can be determined in terms of those caused by the various frequency components of the source functions. The applications of superposition will give us the total fields.
analyze various frequency component  use superposition to get the total field

## Slide 87
Linear system
Linear system
Source: f1
Field: f1
Source
f1
f1
Field
f2
f2
f3
f3
superposition
.
.
.
.
.
.
decomposition

## Slide 88: 7-7.1 The Use of Phasors—A Review
Choose either a cosine or sine function as the reference
Specify 3 parameters: amplitude, frequency, and phase

## Slide 89: Example
The loop equation for a series RLC circuit. Determine i(t)?
Applied voltage
Complicated mathematical manipulations are required to determine I and 
Time domain

## Slide 90: Example
The loop equation for a series RLC circuit. Determine i(t)?
Applied voltage
Phasor domain
Phasors
Phasors contain amplitude and phase information but are independent of t
I. Change to phasor expressions
II. Differentiation and integration
III. Equation in phasor domain
Is can be solved easily.
s(t)=Re[Sejt]
Relation between time-domain and phasor expression

## Slide 91: 7-7.2 Time-Harmonic Electromagnetics
Vector phasors: e.g., a time-harmonic E field
    direction, magnitude, and phase
Differentiation and integration
/t  j

## Slide 92
Maxwell’s equations in terms of vector field phasors (E, H) and source phasors (, J) in a simple (linear, isotropic, and homogeneous) medium
Time-dependent quantities and phasors have the same notations for simplicity.
In the rest of this book, we deal with phasors unless otherwise specified. (Useful note: any quantity containing j must necessarily be a phasor. Any quantities with t must be time-dependent quantities.)
Phasor quantities are not functions of t.

## Slide 93
Time-harmonic wave equations
The Lorentz condition
The phasor solutions for wave equations
where
(the wavenumber)
ej(t-R/u)=ejte-jR/u=ejte-jkR
Time delay (time domain)  additional phase term (phasor domain)
= 2/

## Slide 94
Taylor series expansion of the additional phase term e-jkR
When R<< (or slow variation), e-jkR 1
The solutions for V and A simplify to the static expressions.

## Slide 95: Procedure for Determining E and H due to Time-harmonic  and J
1. Find V and A
2. Find E and B
3. Find instantaneous E(t) and B(t)

## Slide 96: 7-7.3 Source-Free Fields in Simple Media
In a simple, nonconducting source-free medium: =0, J=0, =0
Homogeneous vector Helmholtz’s equations
Method 1
Method 2

## Slide 97
If the medium is conducting (0), J=E0, Eq. with J should be changed.
where
Complex permittivity
If complex permittivity c is used, all the previous equations for nonconducting media can be applied to conducting media.

## Slide 98: Loss
Damping loss: due to out-of-phase polarization
  E is too quick, P is out of phase to E
Ohmic loss: due to free charge carries
The damping and ohmic losses can be characterized in the imaginary part of a complex permittivity c (Chap. 8):
  For an appreciable amount of free charge carriers, ohmic losses dominate and damping losses are very small and already neglected
Comparing

## Slide 99
Low-loss or lossless media: c=’
Lossy media: c=’j’’
Loss tangent: a measure of power loss
The real wavenumber k should be changed to a complex wavenumber kc in a lossy dielectric medium
: loss angle

## Slide 100: A good conductor and a good insulator
A good conductor: >>
A good insulator: >>
Thus, a material may be a good conductor at low frequencies but may have the properties of a lossy dielectric at very high frequencies.
  E.g., moist ground is a relatively good conductor at low frequency and behaves more like an insulator at high frequency.

## Slide 101: 7-7.4 The Electromagnetic Spectrum
Maxwell’s equations, and therefore the wave and Helmholtz’s equations, impose no limit on the frequency of the waves.
All electromagnetic waves in whatever frequency range propagate in a medium with the same velocity:

## Slide 104: Extra slides

## Slide 105
When the secondary winding is terminated in a load resistance RL, the effective load seen by the source

## Slide 106
For a sinusoidal source v1(t) and a load impedance ZL, the effect load seen by the source

## Slide 107
Total flux
Substitution of 1 2 in
where
Self-inductance of the primary winding
Self-inductance of the secondary winding
Mutual inductance
Replace 

## Slide 108: (b) Real transformer
For an ideal transformer:
  Infinite   infinite L
For a real transformer:
k: coefficient of coupling

## Slide 109
A real transformer
  Leakage flux (k<1)
  Noninfinite inductances
  Nonzero winding resistances
  Hysteresis
  Eddy-current losses
  (H)
 An exact analysis is difficult.

## Slide 110
  Leakage flux (k<1) (X1, X2 leakage inductive reactances)
  Nonzero winding resistances (R1, R2 winding resistances)
  Hysteresis (Rc, power loss)
  Eddy-current losses (Rc, power loss)
  (H) (Xc, nonlinear magnetization behavior)
Difficult to analyze…

## Slide 111: Eddy Current
Local currents in the conducting core (normal to )
iEddy
Ohmic power loss (local heating)
One way to reduce undesired eddy-current power loss: high  low  for core materials
High   less reluctance
Low   less current
By Lenz’s law, an eddy current creates a magnetic field that opposes the magnetic field that created it, and thus eddy currents react back on the source of the magnetic field.
less power loss